| Risk Assessment – Specific Activity/Situation |  |
| --- | --- |
| Risk Assessment Reference No: | MO-11-10_19 |

| Workplace Activity: | Using hand tools | Date: | October 2019 |
| --- | --- | --- | --- |

| Persons at Risk- Affected by Activity: | Maintenance Officer | Number | 3 |
| --- | --- | --- | --- |
| Any Vulnerable Persons Affected by Activity: | - | Number | - |

| Setting the Scene: Maintenance officer carrying out maintenance duties in the school using small hand tools such as: Hammer, Screwdrivers, files, spanners, knives etc. |
| --- |
| Potential Hazards | Assessment of Risk |
| Ref. |  | Low | Med | High |
| 1. | Minor and major cuts predominantly to fingers and hands. | X |  |  |
| 2. | A screwdriver used as a chisel could cause the tip to break off and hit the user. | x |  |  |
| 3. | Discarded blades could be found by pupils. |  |  |  |
| 4. | If a wooden handle on a tool such as a hammer is loose, splintered or cracked, the had of the tool may fly off. | X |  |  |
| 5. | A wrench with sprung jaws might slip | X |  |  |
| 6. | The head of a chisel can become ‘mushroomed’ and shatter on impact, sending sharp fragments flying | X |  |  |
| 7. | If users has oil or grease on his hands, the tool may slip during use. In the use of battery tools the switch may be damaged due to oil or grease. |  | X |  |

Existing Control Measures

1. Where there is a risk of cuts to hands or flying debris, use appropriate PPE, such as safety gloves and safety glasses. If you suspect any hand tool is damaged or unsafe take it immediately out of service so it cannot be used. Dispose of it unless it can be fixed – place it in a separate tool storage box until it is fixed. Files: Never use them as levers. Check handles are undamaged and head is secure to the handle.

2. Screwdrivers: Check that you are using the correct screwdriver for the job. Check your drill and charger regularly for loose, broken or melted parts. Chisels: The cutting edge should be sharpened to the correct angle. Carry out termly checks.

3. Cutting tools: Keep knives and blades sharp. Change knife blades in the site office and discard used blades into appropriate container. Maintenance jobs are completed outside of normal school hours whenever possible. Tools are not left in corridors when unattended. Tools are stored in the Maintenance Officers storeroom, which is kept locked at all times.

4. Hammers: check condition of tools on a termly basis. Dispose of hammers with split, broken or loose shafts and worn or chipped heads. Make sure the heads are properly secured to the shafts.

5, 6. Hand tools which can deteriorate with use will be monitored to ensure they are sharpened or replaced as necessary, and that the correct tools are being used properly. Site team do not bring their own tools to use on school premises. All tools are provided by the school.

7. Keep hands clean (oil, grease) when using tools or wear gloves to reduce risk or slipping when holding the tools.

| Initial Assessment of Overall Risk | Low | x | Medium |  | High |  |
| --- | --- | --- | --- | --- | --- | --- |

| RISK RATING = SEVERITY x LIKELIHOOD |
| --- |
| Rating | SEVERITY of injury/disease | LIKELIHOOD of occurrence |
| HIGH | Fatality; major injury or illness causing long term disability | Certain or near certain to occur |
| MEDIUM | Injury or illness causing short term disability | Reasonably likely to occur |
| LOW | Other injury or illness | Unlikely to occur |

| ADDITIONAL CONTROL MEASURES - (IF APPLICABLE) | PERSON RESPONSIBLE FOR IMPLEMENTATION | COMPLETION DATE |
| --- | --- | --- |

| RESIDUAL ASSESSMENT OF OVERALL RISK | LOW | X | MEDIUM |  | HIGH |  |
| --- | --- | --- | --- | --- | --- | --- |

Note:	Re-assessment required if overall residual risk is High

ADDITIONAL INFORMATION: (Notes, comments, further details, outline procedures, safe systems of work, standards, drawings, etc.)

Prepare an inventory list of hand tools. On an annual basis, record the condition of tools being used in school. Look before you drill. Buildings that comply with the National Electric Code should have metal plates covering internal wall wiring, but when drilling into a floor or ceiling, carefully inspect the area for live electrical wires.

| Risk Assessment Circulation List (tick box) |
| --- |
| Employees |  | Management |  | Contractors |  |
| Other – Specify: | MO |  |  |  |  |
| Signature of responsible person: | Date: |
| Assessor: | A Partridge | Signature: |  |
| Date Assessed: | October 2019 | Review Date: | October 2020 |

| RISK ASSESSMENT REVIEW - COMMENTS Date: |
| --- |
| Reason for Review |
| Reviewed By: |  | Signature: |  |

| RISK ASSESSMENT REVIEW - COMMENTS Date: |
| --- |
| Reason for Review |
| Reviewed By: |  | Signature: |  |